## Slide 1
Optimized treatment, recycling and use of degassed biomass as fertilizer
Tyge Kjær
Roskilde University tk@ruc.dk

## Slide 2: Optimized treatment • recycling • use NutriFair 2019 • The 16 January 2019
The biogas plant
Improving of fertilizer product in new and existing biogas plant
Large Scale Bioenergy Lab 2 • NutriFair 2019
Raw materials
Biogas plant
Biogassen
Perhaps two lines:
high quality
loaded line
Residue High quality Use on fields
Combined heat and power (gas engine)
Upgraded biogas to natural gas grid Biogas to industrial processes Biogas to transport
Other applications
Slurry / manure
Additional organic material:
- Residues Agriculture
- deep bedding
- straw
- Residues industry:
Industry
Feed Producer
Residues household
  Organic waste
Green residues
  Including seaweed
Main focus
Gas yield
- Methane/tonne per organic ingredients
- Material contribu- tes to the gas yield
digestion time
Highest possible dry matter level - stirring
The main focus:
Nutrients:
- Nitrogen (4.5-5.0%)
phosphorus
potassium
Carbon content in residue
Residue Load with a.o. heavy metals
()
To the field
To energy plant (combustion)
Organic farming Plougfree farming Precision farming Fertilizer/carbon cycle
—> High vicosity
—> Thick floating layer

## Slide 3: Optimized treatment • recycling • use NutriFair 2019 • The 16 January 2019
The biogas plant
The experiments at Solrød Biogas A/S
Large Scale Bioenergy Lab 2 • NutriFair 2019
Digester 2
Storage tanks
Digester 1
Deflaker
Full scale
Gas mix
Experiments
Biobang
Investigated
AD Boster
Investigated
Separation plant
Separation plant
Enzymer
Full scale
U
U
U+V
U+V
V+F
V+F
V+F
V+F
Supply of normal material
Collection for digestion experiment
Collection for digestion experiment and for viscosity measurement
Collection for viscosity measure- ment & floating layer determination
U
U+V
V+F
U+V
Basic pretreating Experiments
U+V
+ Separation

## Slide 4: Optimized treatment • recycling • use NutriFair 2019 • The 16 January 2019
Succes criteria
The experiments at Solrød Biogas A/S
Low viscosity
Less floating layer
Increase in biogas production (financial basis)
Keeping nutrients in biomass
Large Scale Bioenergy Lab 2 • NutriFair 2019
After pre-treatment
Before pre-treatment

## Slide 5
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019
Circular economy • The food flow
Illustrated with US-materials • Danish conditions are different, but with the same trends
Potentials for Circular economy
Consumed food
Potentials for Circular economy

## Slide 6
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019
The agriculture flow
The linear system
Agri- culture

## Slide 7
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019
The agriculture flow
The circular flow: (1) Nutrients (2) Energy (3) Greenhouse gas reduction
Agri- culture

## Slide 8: Optimized treatment • recycling • use NutriFair 2019 • The 16 January 2019
The circular economy
Block diagram: Circular economy
Large Scale Bioenergy Lab 2 • NutriFair 2019
Crop Production
Input follow production
Husbandry Pig/Cattle
Production of foods
other biological products
Consumption / use Food & Ingredient
Recipient / beach (Aquatic environment)
Substitution of fossils energy
Substitution of fossils energy
Substitution of fossils energy
Substitution of fossils energy
Total N Of this NH4-N
phosphorus potassium The carbon
Energy production Biogas power/heat
CO2 displacement
from organic waste
Greenhouse gas - displa- cement of greenhouse gas
Removing nutrients from the recipient. Reduction of losses of nutrients
Removing nutrients from the recipient.
CO2 displacement from energy consumption
Residues product
Residues product
Life cycle
From cradle to grave
Reduction of nutrients losses
Residues product
Energy Use of biological residues
Input crop Production
Circular economy Biogas plant as »engine«

## Slide 9
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019
Greenhouse gasses (CO2 equivalents)
Prices, Effect and Action plans
Prices: CO2 European Emission Allowances Actual: 22,55 € per tons (January 2019)
Government's climate plan
2018

## Slide 10: Optimized treatment • ecycling • use NutriFair 2019 • The 16 January 2019
Large Scale Bioenergy Lab 2 • NutriFair 2019
Husbandry Pig/Cattle
Product Based Food and ingredients
Consumption / use Food & Ingredient
Recipient / beach (Aquatic environment)
Excipients, energy
Excipients, energy
Excipients, energy
Excipients, energy
Biogas plant
Raw materials 191,000 tons Gas production: 9,3 mio. m3
Slurry: 41.500
Seaweed: 7.400
Total N: 848 tonnes Of this NH4-N: 614 tonnes Phosphorus: 102 tons
Potassium: 234 tons The carbon: 8440 tons
Energy: 6 mio m3 metan - Biogas net: 55.100 MWh
El-production:
22.580 MWh
Heat-production:
27.540 MWh
El/heat: 29.200 tons
The field: 3.100 tons
Organics: 11.900 tons
Greenhouse gas - net: 43.700 tons
Removing nutrients 69-80 tons N, 8,5 ton P
Removing nutrients 75 tons N • 8,5 tons P
3,1
24-31
4,9
7,0
3,6
Economic benefits
in million Danish kroner
Quota price: 22,55 €/tons
Kelco: 79.400
Chr.H: 60.000
? 6,5
8,4
15
Employment
Annual number
5
Operation & maintenance
10
Standard calculation: 240 kr/tons
5,8
Salary
Transport in/out
Solrød Biogas
+ Environment
+ Energy
+ Economy
= Circular economy
Crop Production Input follow production
Turnover: 35 mio.dkr

## Slide 11
Manure: 103.700 tons Deep litter:
4.000 tons Straw/beet tops
11.200 tons
Household waste
1.100 tons
Conventionel
Organic
Sugarbeet tops Straw
Household
Biogas plant
Raw materials:
120.000 tons Gas production:
41.200 MWh Residues:
115.200 tons Nutrients:
827 tons NPK
Gas engine
In: 41.200 MWh
El out:
16.700 MWh
Heat out: 21.600 MWh
El-net
16.700 MWh
District
Heating 10.900 MWh
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019
Recirculation of nutrients
827 tons NPK + Recirculation of Carbon
New Biogas plant
Proposal: 120,000 tons - expected turnover: 21.2 million. Dkr annually
Local economic impact: 24.4 mio. (directly 21.2 mio.)

## Slide 12
New Biogas plant
Proposal: 120,000 tons - expected turnover: 21.2 million. Dkr annually
Local economic impact: 24.4 mio. (directly 21.2 mio.)
Recirculation of nutrients
827 tons NPK + Recirculation of Carbon
Manure: 103.700 tons Deep litter:
4.000 tons Straw/beet tops
11.200 tons
Household:
Sukkeroer
Household
Biogas plant
Råvarer:
Nutrients:
Gas engine
In: 41.200 MWh
El output: 16.700 MWh
Heat output: 21.600 MWh
El-net
16.700 MWh
District heat
Horslunde
10.900 MWh
Heating
5,5 mio kr
Value NPK
6,1 mio kr
FØarkmop. rdordifutct
5,5 mio kr
Salary
1K,4onmvi.odkrrift
1.100Staolnasry trans. 827 tons NPK
1,2 mio kr
120S.0a0la0rytobnisogas
Gaspro1d,u5kmtioion:kr
41.200 MWh Residues:
115.200 tons
Value of
GHG reduction
3,2 mio kr
Large Scale Bioenergy Lab 2 • NutriFair 2019
Optimized treatment • recycling • use
NutriFair 2019 • The 16 January 2019

## Slide 13: Optimized treatment • recycling • use NutriFair 2019 • The 16 January 2019
Large Scale Bioenergy Lab 2 • NutriFair 2019
Thank you for your attention